Date

company name

facility name

Best Management Practices Plan for the Control of Fugitive Dust

Foreword

This Best Management Practices Plan documents the control of fugitive dust at the Company Name Facility Name operations in City, Ontario (the Facility) and has been prepared in accordance with Appendix E (Technical Bulletin - Review of Approaches to Manage Industrial Fugitive Dust Sources) of the Procedure for Preparing an Emission Summary and Dispersion Modelling Report (Ontario Ministry of the Environment 2009) and meets the requirements of Section XX of Certificate of Approval No. XXXX-XXXXXX issued on date of issue.

This document updates and replaces all previous versions of fugitive dust control plans for the Facility issued prior to and including date of report.

As operations change and new fugitive dust sources are added to the Facility, this Plan will be updated as required.  In order to maintain version control all pages in the Plan have been dated and documented with a version number.  This Plan is Version 1.0.  The version number will change if the entire report is reissued; if individual pages are provided to update small portions of the Plan then they will be issued with a .X subversion number and the updated pages will be listed on the following Version Control Page.

Version Control

| Version | Date | Description of Changes | Updated Pages | Approved By Job Title | Approved By Sign Off |
| --- | --- | --- | --- | --- | --- |

Table of Contents

1.0	INTRODUCTION	1

2.0	Facility Description	4

3.0	Responsibilities	5

3.1	Senior Management Representative:  Mine Manager	5

3.2	Accountable Site Representative:  Superintendent – Production	5

3.3	Unit Operations Supervisor:  Supervisor – Production	5

3.4	Site Personnel and Contractors	5

4.0	Fugitive Dust Emissions best management practices Plan	6

4.1	PLAN – Identification and Classification of Fugitive Dust Emission Sources	6

4.1.1	Identification of the Sources of Fugitive Dust Emissions	6

4.1.2	Fugitive Dust Characterization	7

4.1.3	Fugitive Dust Best Management Practices	11

4.2	DO – Implementation Schedule for the BMP Plan	12

4.2.1	Training	12

4.3	CHECK – Inspection, Maintenance and Documentation	12

4.4	ACT – BMP Plan Review and Continuous Improvement	13

References	14

Tables

Table 1: Facility description	4

Table 2: Sources of fugitive dust emissions within the Facility and potential causes for high emissions	6

Table 3: Facility Name road dust sampling silt content analysis results	8

Table 4: Facility Name road dust sampling metals analysis results	8

Table 5: Description of preventative procedures and control measures for fugitive dust emissions existing and under development at the Facility	11

Table 6: Fugitive dust sources and associated relative risk scores	11

Table 7: Implementation process for new emission sources	12

Table 8: Inspection frequency summary	13

Table 9: Inspection documentation for the Facility organized by emission source type	13

Figures

Figure 1 – Fugitive Dust Sources Location Plan

appendices

APPENDIX A

Ministry Comments

APPENDIX B

Road Dust Sampling Technical Memo

APPENDIX C

Fugitive Dust Source Risk Ranking

APPENDIX D

Start Up Checklists

APPENDIX E

Dust Control Inspection Form

APPENDIX F

Dust Control Activity Log Sheets

APPENDIX G

Non-Conformance Log

# INTRODUCTION

The purpose of this Plan is to document the Best Management Practices (BMPs) for the control of fugitive dust emissions from Company Name’s Facility Name (the Facility) and outline the decision making process that was used to develop these BMPs.  This Plan was prepared in accordance with Appendix E (Technical Bulletin - Review of Approaches to Manage Industrial Fugitive Dust Sources) of the Procedure for Preparing an Emission Summary and Dispersion Modelling Report (January 2004) and meets the requirements of Section XX of Certificate of Approval No. XXXX-XXXXXX issued on date of issue.

7.0 FUGITIVE DUST CONTROL

7.1 The Company shall develop in consultation with the District Manager and acceptable to the Director, a Best Management Practices Plan for the control of fugitive dust emissions. This Best Management Practices Plan shall include, but not be limited to:

(1) identification of the main sources of fugitive dust emissions such as:

(a) on-site traffic;

(b) paved roads/areas;

(c) unpaved roads/areas;

(d) material stock piles;

(e) loading/unloading areas and loading/unloading techniques;

(f) material spills;

(g) material conveyance systems;

(h) exposed openings in process and storage buildings; and

(i) general work areas.

(2) potential causes for high dust emissions and opacity resulting from these sources;

(3) preventative and control measures in place or under development to minimize the likelihood of high dust emissions and opacity from the sources of fugitive dust emissions identified above. Details of the preventative and control measures shall include:

(a) a description of the control equipment to be installed;

(b) a description of the preventative procedures to be implemented; and/or

(c) the frequency of occurrence of periodic preventative activities, including material application rates, as applicable.

(4) an implementation schedule for the Best Management Practices Plan, including training of facility personnel;

(5) inspection and maintenance procedures and monitoring initiatives to ensure effective implementation of the preventative and control measures; and

(6) a list of all Ministry comments received, if any, on the development of the Best Management Practices Plan, and a description of how each Ministry comment was addressed in the Best Management Practices Plan.

7.2. The Company shall submit the Best Management Practices Plan to the Director and the District Manager not later than six months after the date of this Certificate.

(1) The Director may not accept the Best Management Practices Plan if the minimum requirements described in Condition No. 7.1 were not included in the Best Management Practices Plan.

(2) If the Best Management Practices Plan is not accepted by the Director, the Company shall submit a Best Management Practices Plan acceptable to the Director not later than nine months after the date of this Certificate;

7.3. Upon acceptance of the Best Management Practices Plan by the Director, the Company shall immediately implement the Best Management Practices Plan for the control of fugitive dust emissions to provide effective dust suppression measures to any potential sources of fugitive dust emissions resulting from the operation of the Facility.

Documentation Requirements - Best Management Practices Plan

7.4. The Company shall record, in a log book, each time a specific preventative and control measure described in the Best Management Practices Plan is implemented. The Company shall record, as a minimum:

(1) the date when each emission control measure is installed, including a description of the control measure;

(2) the date when each new preventative measure or operating procedure to minimize emissions is implemented, including

a description of the preventative measure or operating procedure; and

(3) the date, time of commencement, and time of completion of each periodic activity conducted to minimize emissions, including a description of the preventative measure/procedure and the name of the individual performing the periodic activity.

This Plan will:

identify the sources of fugitive dust emissions associated with the Facility;

review the composition and size distribution of the fugitive dust particulate including an analysis of the metals composition of the road dust;

describe how fugitive dust can be controlled from each significant source and describe the BMPs in place at the Facility;

contain a schedule by which the Plan will be implemented;

describe how the Plan will be implemented, including the training of personnel;

describe inspection and maintenance procedures;

describe methods of monitoring and record-keeping to verify and document ongoing compliance with the Plan.

For ease of implementation and to promote clarity, this Plan follows the following structure:

Section 2 provides a brief description of the Facility.

Section 3 documents the BMPs that are in place at the Facility and the decision making process used to develop these BMPs  This section follows the Plan Do Check and Act (PDCA) cycle according to ISO guidelines.  The “Plan” section includes identification and characterization of the emission sources and existing BMPs at the Facility.  The “Do” section includes a schedule for implementation of the proposed improvements.  The “Check” section includes a description of monitoring procedures and a recordkeeping system.  The “Act” section includes guidelines for periodic review of the BMPs in order to promote its continuous improvement.

Ministry comments pertaining to the development and maintenance of this Plan are included in Appendix A.

# Facility Description

Company Name operates a Facility Type located at Facility Address in City, Ontario (the Facility).  Table 1 presents general information about the Facility relevant to this Plan.

Table 1: Facility Description

| Facility: |  |
| --- | --- |
| Location: |  |
| Area occupied: |  |
| Main activities/ equipment used: |  |
| Production: |  |
| Nearest sensitive receptors (distance/ direction): |  |
| Predominant wind direction: |  |

Figure 1 is a site plan showing the fugitive dust sources present onsite and the location of nearest receptors.

# Responsibilities

The following identifies the responsibilities held by each of the employment levels at the Facility as they pertain to this Plan.

## Senior Management Representative:  Mine Manager

The Senior Management Representative, or designate, is responsible for:

reviewing the effectiveness of the current dust control measures at the Facility; and

ensuring the required resources are in place to execute the plan.

## Accountable Site Representative:  Superintendent – Production

The Accountable Site Representative, or designate, is responsible for:

reviewing the effectiveness of the current dust control measures at the Facility;

scheduling and coordinating the implementation of fugitive dust control measures;

maintaining documentation of schedules and logs; and

ensuring the training of site personnel and contractors on the plan and best management practices to be implemented.

## Unit Operations Supervisor:  Supervisor – Production

The Unit Operations Supervisor is responsible for:

reviewing the effectiveness of the current dust control measures at the Facility;

implementing fugitive dust control measures; and

completing dust control logs.

## Site Personnel and Contractors

All Site Personnel and Contractors are responsible for:

reviewing the effectiveness of the current dust control measures at the Facility; and

following the dust control procedures that are currently in place.

# Fugitive Dust Emissions best management practices Plan

This section describes the fugitive dust control measures that are implemented at the Facility and the decision making process that has been used in the BMP development for the Facility.  This section follows the Plan Do Check and Act (PDCA) cycle according to ISO guideline as follows:

- Section 4.1   PLAN - identifies and characterizes the emission sources and BMPs at the Facility.

- Section 4.2   DO - documents the schedule for implementation of the proposed improvements.

- Section 4.3   CHECK - describes the monitoring procedures and a recordkeeping system.

- Section 4.4   ACT - describes the BMP review and update procedures in order to promote its continuous improvement.

## PLAN – Identification and Classification of Fugitive Dust Emission Sources

### Identification of the Sources of Fugitive Dust Emissions

Fugitive dust emissions occur due to mechanical disturbances of granular materials exposed to the air. Dust generated from these open sources is termed “fugitive” because it is not discharged to the atmosphere in a confined flow stream, such as in an exhaust pipe or stack (USEPA 1995).

The mechanical disturbance may be equipment movement, the wind or both. Therefore, some fugitive dust emissions occur and/or are intensified by equipment use, while others, i.e. wind erosion emissions, are independent of equipment use.

The main factors affecting the amount of fugitive dust emitted from a source include characteristics of the granular material being disturbed (i.e. particulate size distribution, density and moisture) and intensity and frequency of the mechanical disturbance (i.e. wind conditions and/or equipment use conditions). Precipitation and evaporation conditions can affect the moisture of the granular material being disturbed and, therefore, have an indirect effect on the amount of fugitive dust emitted.

Once dust is emitted, its travelling distance from the source is affected by various parameters.  Namely climatic conditions, specifically wind speed, wind direction and precipitation, and particle size distribution.  Higher wind speeds increase the distance travelled while precipitation can accelerate its deposition. Finer particulates can travel longer before settling and, therefore, deserve major concern.

Table 2 presents a summary of the main sources of fugitive dust emissions existing at the Facility, as well as the potential causes for high dust emissions and opacity resulting from these sources.

Table 2: Sources of Fugitive Dust Emissions within the Facility and Potential Causes for High Emissions

| Identification of Sources of Fugitive Dust Emissions | Potential Causes for High Emissions and Opacity from Each Source (Parameters/Conditions) |
| --- | --- |
| Source Category | Source Description | Source Location |  |

### Fugitive Dust Characterization

Fugitive dust sampling was conducted at the Facility in date of sampling.  A technical memo outlining the sampling procedure and showing the full results of the sampling is included in Appendix B.

The following tables show a comparison between the Facility’s road dust and typical metals concentrations in Ontario identified in the literature review document (Golder 2010).

The maximum silt content for the Facility’s unpaved roads is slightly above the mean value for Ontario mine sites, however, it is well below the maximum.  For paved roads, the maximum Facility silt content is below the mean value for Ontario mine sites.  For the metals concentrations, all the Facility’s maximum concentrations are around the mean value for Ontario mine sites.

Table 3: Facility Name Road Dust Sampling Silt Content Analysis Results

| Silt Content | Facility Name SAMPLING RESULTS | ONTARIO MINING SITES |
| --- | --- | --- |
|  | Unpaved Roads | Paved Roads | Unpaved Roads | Paved Roads |
|  | Maximum | Maximum | Maximum | Minimum | Mean | Maximum | Minimum | Mean |
| (%) |  |  | 36.80 | 0.10 | 9.14 | 35.60 | 0.72 | 3.55 |
| (g/m²) |  |  | 282.00 | 1.21 | 34.30 | 18.85 | 0.00 | 0.18 |

Table 4: Facility Name Road Dust Sampling Metals Analysis Results

| METAL | Facility Name SAMPLING RESULTS | ONTARIO STUDIES | ONTARIO MINING SITES |
| --- | --- | --- | --- |
|  | Unpaved Roads (µg/g) | Paved Roads (µg/g) | Ontario Typical Range¹ (µg/g) | Unpaved Roads (µg/g) | Paved Roads (µg/g) |
|  | Maximum | Maximum | 98th perc | Maximum | Minimum | Mean | Maximum | Minimum | Mean |
| Aluminum |  |  | 30000 | 64000 | 179 | 10135 | 15900 | 718 | 4870 |
| Antimony |  |  | 0.43 | 210 | 0.5 | 4.95 | 88.7 | 0.41 | 8.45 |
| Arsenic |  |  | 17 | 34000 | 0.5 | 89.7 | 1140 | 2.8 | 64.05 |
| Barium |  |  | 180 | 580 | 1.2 | 51.3 | 173 | 5.45 | 46.6 |
| Beryllium |  |  | 1.1 | 1 | 0.24 | 0.5 | 7.1 | 0.4 | 0.5 |
| Bismuth |  |  | — | 116 | 0.54 | 3 | 192 | 1.2 | 17.5 |
| Boron |  |  | 30 | 35.8 | 1 | 5.8 | 16 | 1 | 3.8 |
| Cadmium |  |  | 0.84 | 16.6 | 0.05 | 1.29 | 28.6 | 0.4 | 1.65 |
| Calcium |  |  | 58000 | 72000 | 100 | 9400 | 7240 | 513 | 3220 |
| Cerium |  |  | — | 153 | 0.81 | 24.65 | 52.7 | 5.32 | 22 |
| Cesium |  |  | — | 1.5 | 0.49 | 0.74 | 0.78 | 0.43 | 0.57 |
| Chromium |  |  | 62 | 410 | 1.5 | 90.2 | 418 | 11.7 | 81.5 |
| Cobalt |  |  | 17 | 4950 | 2.29 | 130 | 10400 | 35.6 | 382 |
| Copper |  |  | 65 | 50300 | 49.1 | 1570 | 174000 | 200 | 11700 |
| Europium |  |  | — | 1.9 | 0.49 | 0.64 | 0.55 | 0.49 | 0.55 |
| Gallium |  |  | — | 7.88 | 0.66 | 4.4 | 6.7 | 0.61 | 3.9 |
| Iron |  |  | 35000 | 143000 | 1140 | 63500 | 177000 | 13200 | 50100 |
| Lanthanum |  |  | — | 85.3 | 2.7 | 11.6 | 29.9 | 2.5 | 10 |
| Lead |  |  | 98 | 721 | 2.3 | 41.8 | 993 | 14.4 | 131 |
| Lithium |  |  | — | 45 | 4.2 | 12.5 | 13 | 5.9 | 7 |
| Magnesium |  |  | 20000 | 47000 | 125 | 7080 | 6940 | 502 | 4020 |
| Manganese |  |  | 2200 | 2300 | 5.04 | 310 | 1180 | 36 | 195 |
| Mercury |  |  | 0.18 | 0.758 | 0.049 | 0.24 | 1.2 | 0.04 | 0.455 |
| Molybdenum |  |  | 1 | 25.2 | 0.55 | 4.45 | 72 | 0.69 | 8.34 |
| Nickel |  |  | 38 | 488000 | 14.5 | 1580 | 429000 | 133 | 10400 |
| Niobium |  |  | — | — | — | — | 4.4 | 0.72 | 2.56 |
| Phosphorus |  |  | — | 1000 | 92 | 360 | 833 | 68 | 340 |
| Rubidium |  |  | — | 37.4 | 1.2 | 10 | 18.5 | 0.99 | 6.4 |
| Scandium |  |  | — | 8.38 | 0.59 | 3.2 | 3.9 | 0.86 | 2.6 |
| Selenium |  |  | 1.3 | 89.9 | 0.5 | 7.7 | 154 | 1.2 | 25.55 |
| Silver |  |  | 0.33 | 131 | 0.052 | 1.47 | 139 | 0.4 | 9.06 |
| Strontium |  |  | 78 | 184 | 2.6 | 55.2 | 79.5 | 4 | 23 |
| Thallium |  |  | 0.81 | 0.59 | 0.59 | 0.59 | — | — | — |
| Thorium |  |  | — | 22.4 | 1.4 | 7.4 | 21.3 | 1.7 | 5.02 |
| Tin |  |  | — | 230 | 0.5 | 7.72 | 327 | 1.6 | 26 |
| Titanium |  |  | 5200 | 3400 | 18.2 | 870 | 1180 | 124 | 708 |
| Tungsten |  |  | — | 12.5 | 0.57 | 3.2 | 104 | 0.49 | 12 |
| Uranium |  |  | 2.1 | 6.8 | 0.49 | 0.965 | 1.6 | 0.71 | 1.1 |
| Vanadium |  |  | 77 | 220 | 0.5 | 44.7 | 55 | 6.69 | 32.35 |
| Yttrium |  |  | — | 52.2 | 1.1 | 6.725 | 10 | 0.72 | 4.45 |
| Zinc |  |  | 140 | 4400 | 5 | 220 | 1250 | 39.1 | 282 |
| Zirconium |  |  | — | 16.5 | 0.58 | 4.9 | 15.6 | 1.3 | 4.45 |

Notes:

¹ 	Ontario Ministry of the Environment and Energy 1993

- no data

ND	not detectable

### Fugitive Dust Best Management Practices

Control measures to reduce fugitive dust emissions should take into account the sources of the dust emission, the dispersion conditions and the location of sensitive areas in order to avoid relevant impacts of dust emissions on receptors.

Control measures intend to affect one or more factors affecting the generation and/or dispersion of fugitive dust emissions.  These control measures can be classified as follows;

Preventative Procedure: Measure pertaining to the design and installation of structures and the operating procedures which are implemented on a regular basis in order to prevent the generation of dust and/or the dispersion of dust emitted reaching sensitive areas.

Reactive Control Measures: Measures which are implemented in the event of unexpected circumstances which can lead to the generation of dust and/or the dispersion of dust emitted reaching sensitive areas.

Table 5 presents Preventative Procedures and Reactive Control Measures for fugitive dust emissions that are associated with the Facility Name.

Table 5: Description of Preventative Procedures and Control Measures for Fugitive Dust Emissions Existing and Under Development at the Facility

| Emission Source | Preventative Procedure/ Control Measure | Description | Frequency |
| --- | --- | --- | --- |

Each fugitive dust source at the Facility was assessed using the risk management tool described in the guidance document (CEMI 2010) to assess if the BMPs that are in place adequately manage the risk associated with each source.  See Appendix C for the risk factors used in the ranking process.  The following table identifies all fugitive dust sources with their respective relative risk score for the Facility.

Table 6: Fugitive Dust Sources and Associated Relative Risk Scores

| Source ID | Source Description | BMP (if any) | Relative Risk Score | Relative Risk Level |
| --- | --- | --- | --- | --- |

There are no sources that are still considered to be “high” risk after the implementation of the BMPs therefore it is assumed that the BMPs in place adequately manage the risk associated with each fugitive dust source.

## DO – Implementation Schedule for the BMP Plan

All of the BMPs listed in Table 5 have already been implemented at the Facility.

All dust generating work performed onsite, whether it is being completed by Company or under contractual agreements, must conform to the requirements of this Plan.

Table 7 presents the process for the implementation of any new BMP for control of fugitive dust emissions at the Facility, as well as the corresponding start-up checklist that is to be completed.  The purpose of the checklists is to ensure that the new emission source will be implemented following that same dust control procedures of the current sources at the Facility.  Examples of the checklists are presented in Appendix D.

Table 7: Implementation Process for New Emission Sources

| New Emission Source | Examples | Start-up Checklists |
| --- | --- | --- |

### Training

All site personnel and contractors are to receive training on the requirements of this Plan.  Training will be incorporated into the Facility indoctrination that is required prior to working on the property.  These training records will be kept with all other training records in the training department.

## CHECK – Inspection, Maintenance and Documentation

An inspection of the conformity with the BMPs will be documented weekly using the Dust Control Inspection Form (see Appendix E for an example form).  Each dust emission source type has a corresponding log sheet (see Appendix F) to record all dust control activity pertaining to those sources.

In the event of a non-conformance, the inspector will add the incident to the Non-Conformance Log (see Appendix G).  Corrective action is to be taken to eliminate the causes of the non-conformance.  It is expected that all deficiencies identified in inspections be addressed immediately.  Reviews of the Non-Conformance Logs will be done quarterly as part of the BMP continuous improvement program, explained in more details in Section 4.4.

Table 8 provides a summary of the inspections that take place at the site under this Plan and the inspection frequency.

Table 8: Inspection Frequency Summary

| Inspection Type | Frequency |
| --- | --- |

Table 9 presents all the inspection and maintenance procedures in place and the respective documentation to support ongoing conformity with preventative and control measures described in the Table 5 for each emission type.

Table 9: Inspection Documentation for the Facility Organized by Emission Source Type

| Dust Emission Source Type | Documentation | Document Control/ Recordkeeping |
| --- | --- | --- |

As part of recordkeeping procedures the above information should be recorded in electronic files and hard copies, for a minimum period of seven years.  The Production Superintendent is responsible for recordkeeping the information listed above and copies of all documents are kept in the Document Name which is kept on the red shelving unit in the Production Superintendent’s office.

## ACT – BMP Plan Review and Continuous Improvement

Inspections and monitoring procedures will assist Company personnel with the maintenance of an effective BMP Plan.  The BMP Plan should be monitored and updated, as follows:

when there are significant changes in the fugitive dust emissions sources;

periodically, every five years (minimum);

when there are verified complaints associated with fugitive dust emissions from the Facility; and

when there are visible dust emissions occurring more frequently and/or at a higher rate (excluding seasonal conditions).

Review of the BMP Plan is intended to evaluate the effectiveness of the dust control practices and focus on the identification of improvement opportunities that can reduce the risk of complaints related to fugitive dust emissions.

# References

Centre for Excellence in Mining Innovation.  2010.  Guide to the Preparation of a Best Management Practices Plan for the Control of Fugitive Dust for the Ontario Mining Section.  Version 1.0, August 2010.

Golder Associates Ltd.  2010.  Literature Review of the Current Fugitive Dust Control Practices within the Mining Industry.  August 11, 2010.

Ontario Ministry of the Environment.  2004.  Review of Approaches to Manage Industrial Fugitive Dust Sources. January 2004.

Ontario Ministry of the Environment.  2009.  Procedure for Preparing an Emission Summary and Dispersion Modelling Report – Version 3.0. March 2009.

Ontario Ministry of the Environment and Energy.  1993.  Ontario Typical Range of Chemical Parameters in Soil, Vegetation, Moss Bags and Snow, December 1993.

United States Environmental Protection Agency (USEPA).  1995.  AP-42 – Compilation of Air Pollutant Emission Factors – Fifth Edition. January 1995.

Ministry Comments

Road Dust Sampling Technical Memo

Fugitive Dust Source Risk Ranking

Start Up Checklists

Dust Control Inspection Form

Dust Control Activity Log Sheets

Non-Conformance Log

# Text boxes

| Reference Number: | XXXXXXXXX |  |
| --- | --- | --- |