## Slide 1: Presentation of the waste heat recovery simulator for the mining sector
20th October 2021,
Yan Germain, ing. and Enrique Acuna-Duhart, PhD
CanmetMINING
Organized by: The Centre for Excellence in Mining Innovation (CEMI)

## Slide 2: Contents
Introduction
How does the simulator work?
Simulator input and output parameters
Simulation example
Next steps

## Slide 3: 1. Introduction What is the problem and the opportunity?
The problem :
  The mining sector consumes a large amount of energy in these mining operations;
  Most of the systems used in mining operations have poor energy yields;
  A large part of the energy consumed is therefore usefully transformed into residual energy in the form of thermal energy;
  This residual energy is mainly absorbed by the pulp during mining treatment or lost in the environment (conduction, convection, evaporation, etc.);
The opportunity :
  The presence of a large amount of residual energy in the sector favors the integration of residual energy recovery techniques;
  These techniques make it possible to improve residual energy by reusing it on complementary systems and reduce their:
    Energy consumption (electricity and fuel)
    Greenhouse gas (GHG) emissions
The recovery of residual energy on mining sites is a good example of sustainable development that benefits the environment.

## Slide 4: 1. Introduction Basis of waste energy recovery
The basic principle of waste energy recovery is to recover the waste heat (energy) from a system and reusing it to provide energy to a complementary system.
The recovery of waste energy involves the use of at least two systems operating in symbiosis; one of the systems provides the energy and is considered a "source" system and the second consumes the energy and is considered a "load“ system.
Energy recovery can be summed up in 3 steps:
  Capture of residual heat available in the “source’’ system:
  The transfer of captured energy to the ‘’load’’ system:
  The reuse of energy by the ‘’load’’ system. This reuse decreases the energy consumed by the system.
Step : 2
Step : 1
Step : 3

## Slide 5: 1. Introduction Example of energy recovery between two systems
Note:
The theoretical thermal power that can be transferred corresponds to the minimum power between the amount available from the "source" system and the thermal power consumed by the "load" system.
Addition of equipment to capture energy
Addition of equipment to reuse energy
Useful energy
Useful energy
Effective energy
Raw energy
Fan
Fan
Return air
Supply
Evacuation
Outdoor air intake
Residual energy
Energy transport
Heat transfer network

## Slide 6: 1. Introduction Equipment used in energy recovery
Plate heat exchanger (water / water)
Coil (water / air)
Exchanger (air / air)
Heat pump (water / air)
Heat pump (water / water)
Combustion exchanger (air / gas)
Référence : https://www.enviroair.ca/
Note:
There are many types energy recovery equipment on the market. The selection of equipment should always be made by a competent person in the field and take into account the system we would like to add.

## Slide 7: 1. Introduction The challenge with residual energy recovery
Question :
How can we predict the effect of adding a system on energy savings?
Issues :
The power that can be transferred depends on the operating conditions of both systems;
Systems can operate independently which influences energy transfer;
Some systems have operating temperatures that vary throughout the year which affects the energy that can be transferred between systems;
Energy transfer
???

## Slide 8: 2. How does the simulator work? Purpose of the simulator and functional diagram
Purpose of the simulator
Analyze the annual energy transfer that could exists with the combination of different systems as part of an energy recovery project. The simulator makes it possible to calculate:
The energy savings achieved on "load" systems;
The preliminary sizing of the equipment to be integrated into the systems;
The preliminary performance of the heat transfer network;
Reduction of greenhouse gases emissions
Type # 1
System selection and general information on the heat transfer network
Information from "source" systems
Information of "load" systems
Energy simulator
Energy recovery performance and GHG savings
Preliminary sizing of equipment
Sizing and performance of the heat transfer network
Output parameters
Input parameters
Type # 2
Type # 3
Type # 4
Type # 1
Type # 2
Type # 3

## Slide 9: 2. How does the simulator work? Characteristics of the simulator
Program considerations,
“Excel” program platform;
Program adapted for the mining sector;
Energy analysis carried out for a full year;
Energy analysis carried out on an hourly basis; 8,760 iterations (each hour of the year);
Takes into account the performance and operating temperatures of "source" and "load" systems;
Takes into account the climate conditions of the mining site;
Takes into account the performance of the equipment to be incorporated into the system;
Can consider several "source" and "load" systems in the analysis;
Can consider the use of a heat pump as equipment to reuse residual energy towards "load" systems.
Program limitation
Limited types of "source" and "load" systems;
Considers operating hours running 24 hours a day (if necessary);
The simulator performs its analysis according to a standardized temperature profile in accordance with the geographical position of the site;
The simulator considers constant operating conditions as input parameters.

## Slide 10: 2. How does the simulator work? Type of "source" and "load" systems included in the simulator
Type of "source" systems (4 types)
Type of "load" systems (3 types)
Type 1 : Filtration system for ore processing plants
Type 2 : Hot fluid discharge system
Type 3 : Technical room cooling system
Type 4 : Equipment cooling system mechanical / electrical
Type 1 : Forced air heating system for buildings
Type 2 : Fresh air heating system
Type 3 : Water heating system

## Slide 11: 2. How does the simulator work? Simulator analysis methodology
Simulator methodology
Modeling of theoretical powers and operating temperatures of "source" and "load" systems;
Selection of the systems that we would like to combine with each other as part of an energy recovery project;
Analysis of the heat transfer network operating conditions to satisfy the power balance between the "source" and "load" systems;
Analysis of the transferred power considering the performance of the heat exchangers added to the systems and calculation of energy costs;
TFC : Hot network temperature (°C)
TFF : Cold network temperature (°C)
C : Flow capacity on the network side (kW / °C)
NTU : Number of transfer units for heat exchanger
Note : The simulator methodology is performed for each hour of the year.
Type # 1
1 system
Type # 2
3 systems
Type # 3
1 system
Type # 1
1 system
Type # 2
3 systems
Type # 3
1 system
Type # 3
1 system

## Slide 12: 3. Simulator input and output parameters Input parameters for type 1 "source" system
Facility operating condition |  | 
Description | Variable | Value
Average mass flow rate at the inlet of the plant (t/day) | mr | Value
Thermal capacity of the ore at the entrance to the plant (kJ/kg°C) | CPR | Value
Variation of the mass flow rate at the entrance to the plant (± %) | VAR | Choice 0 to 10 %
Average percent moisture contained in the ore at the entrance to the concentrator | %HR | Choice 0 to 10 %
Percent solids of pulp after thickener (%) | %SEP | Choice 40 to 80 %
Percent solids of pulp at the plant discharge (%) (<= %SEP) | %SOUT | Choice 10 to 70 %
Percentage of fresh water used in the treatment plant in relation to the volume of water lost (0 < Ra < 100%) | RA | Choice 0 to 100 %
Percentage of additional water used by other areas compared to the volume of water lost to the tailings pond (0 < RB < 200%) | RB | Choice 0 to 200 %
Minimum water temperature observed at the outlet of the plant during the year (°C) | TOUT,min | Choice 10 to 40°C
Minimum process water temperature after energy transfer(°C) | TH,O_MIN | Choice 1 to 15°C
Maximum ore temperature during summer(°C) | TR_MAX | Value
Minimum ore temperature during winter (°C) | TR_MIN | Value
Filtration system of an ore processing plant
(1 system available in the simulator)
(QS1)
Ore processing plant system

## Slide 13: 3. Simulator input and output parameters Input parameters for type 2 and 3 "source" systems
Hot fluid discharge system
(3 systems available in the simulator)
(QS2A, QS2B et QS2C)
Technical room cooling system
(1 system available in the simulator)
(QS3)
Information on the equipment in the room |  | 
Type of equipment installed in the room (10 equipments possible) | Power (kW) | 
Equipment # 3 (choice) | Value | 
Equipment # 3 (choice) | Value | 
**** | *** | 
Equipment # 3 (choice) | Value | 
Operating conditions of new ventilation system |  | 
Room temperature set point(°C) | TAMB | Choice
Ventilation system temperature difference (°C) | ∆T | 5 to 25
Equipment options
Transformer
Variable speed drive
Generator (loss irradiating in the room)
Generator (losses from radiator)
Electric motor
Compressor
Description | Variable | Discharge A | Discharge B | Discharge C
Fluid type | type | Choice Air / water | Choice Air / water | Choice Air / water
Flow (L/s) | D | Value | Value | Value
Fluid temperature before cooling (°C) | TEVA | Value | Value | valeur
Minimum fluid temperature after cooling (°C) | TREF | Choice 10 to -20 or Text | Choice 10 to -20 or Text | Choice 10 to -20 or Text

## Slide 14: 3. Simulator input and output parameters Input parameters for type 4 "source" systems
Mechanical / electrical equipment cooling system
(1 system available in the simulator)
(QS4)
Information of the equipment used |  | 
Equipment type | Power (kW) | 
Type of equipment (choice) | Value | 
Equipment cooling system information |  | 
Description | Variable | Value
Temperature of the hot fluid entering the equipment cooling system (°C) | Th,i | value
Temperature difference between the inlet and outlet of the equipment cooling system (°C) | ∆T,EC | Choice 12 to 24
Type of fluid used by the cooling system | type | Choice
Types of equipment considered by the simulator | Fluid types considered by the simulator
Transformer | Water
Variable speed drive | Engine oil
Generator (radiator losses) | Ethylene glycol
Generator (exhaust gas losses) | Refrigerant -134a
Mill system trunnion | Refrigerant -22

## Slide 15: 3. Simulator input and output parameters Input parameters for type 1 and 2 "load" systems
Building heating system (centralized air system)
(1 system available in the simulator)
(QC1)
Heating system information |  | 
Description | Variable | Value
Maximum heating power required to heat the building (kW) | QMAX | Value
Supply temperature of the building ventilation system (°C) | TALIM | Value
Average temperature maintained inside the building (°C) | TIN | Value
Air supply systems information |  |  |  | 
Description | Variable | Sup #A | Sup #B | Sup #C
Ventilation flow (L/s) | DVENT | Value | Value | Value
Supply temperature (°C) | TALM | Value | Value | Value
Building heating system (100% fresh air system)
(3 systems available in the simulator)
(QC2A, QC2B and QC2C)

## Slide 16: 3. Simulator input and output parameters Input parameters for type 3 "load" systems
Water heating system
(1 system available in the simulator)
(QC3)
Hot water consumption information |  | 
Description | Variable | Value
Shower head type | CSTD | Choice of 4 types of standard heads
Number of shower heads (unit) | NEQ | Value
Equipment usage time during activation (min) | ∆t | Choice 5 to 60
Number of activations per day | K | Choice 1 to 4
Water heater temperature set point (°C) | TE | Value
Shower water temperature (°C) | T1 | Choice 30 to TE
Average water consumption in other areas (L/h) | D2 | Value
Water temperature used in other areas (°C) | T2 | Choice 30 to TE

## Slide 17: 3. Simulator input and output parameters Input parameters associated with energy transfer
Selection of « source » systems |  |  |  |  |  | 
System | QS1_EP | QS2A | QS2B | QS2C | QS3 | QS4
Source selection | (Choice) Yes /no | (Choice) Yes /no | (Choice) Yes /no | (Choice) Yes /no | (Choice) Yes /no | (Choice) Yes /no
Number of transfer units for exchanger (NTU) | (Choice) 0 to 5 | (Choice) 0 to 5 | (Choice) 0 to 5 | (Choice) 0 to 5 | (Choice) 0 to 5 | (Choice) 0 to 5
Selection of « load » systems |  |  |  |  | 
System | QC1 | QC2A | QC2B | QC2C | QC3
Load selection | Yes /no | Yes /no | Yes /no | Yes /no | Yes /no
Type of energy consumed by the load | (Choice) listing | (Choice) listing | (Choice) listing | (Choice) listing | (Choice) listing
Number of transfer units for exchanger (NTU) | (Choice) 0 to 5 | (Choice) 0 to 5 | (Choice) 0 to 5 | (Choice) 0 to 5 | (Choice) 0 to 5
Use of a heat pump | (Choice) Yes /no | (Choice) Yes /no | (Choice) Yes /no | (Choice) Yes /no | (Choice) Yes /no
Type of energy available for "load" systems | 
Electricity (kWh) | kWh
Propane (L) | Litre
Natural gas (m³) | m3
Diesel (L) | Litre
City temperature profiles included in the simulator
Val-d'Or - Québec
Kelowna - British Columbia
Sudbury - Ontario
Timmins - Ontario
Thompson - Manitoba
Corner Brook - Newfoundland and Labrador
La Grande - Québec
Éléonore - Québec

## Slide 18: 3. Simulator input and output parameters Input parameters associated with the heat transfer network
Heat transfer network information |  | 
Description | Variable | Value
Type of glycol mixture used the heat transfer network (ethylene / propylene) | K | (Choice) Ethylene / propylene
Safety factor for calculating the pressure drop of the glycol network | F.S. | (Choice) 0 to 100%
Efficiency of the glycol network pump | Rpom | Choice 0 to 100%
Distance between thermal source and load [m] | DIS | Value
Pipe size selected Note: The simulator provides the minimum size required for the main pipe | Ө | (Choice) 50, 100, 150, 200, 250 et 300 mm
TFC : Hot temperature entering the heat transfer network (°C)
TFF : Cold temperature entering heat transfer network (°C)
C : Flow capacity of the heat transfer network (kW/°C)
NTU : Number of transfer units for heat exchanger

## Slide 19: 3. Simulator input and output parameters Example of simulator result and information blocks
Information block available - "Association" tab of the program
Balance of energy available in "source" systems;
Assessment of greenhouse gas (GHG) consumption and emissions from "load" systems;
Simplified diagram of energy transfer between systems and information related to climatic temperatures;
Balance of energy transfer, additional energy consumed by the use of heat pumps and the GHG savings produced by the transfer of energy between the selected systems;
Assessment of the heat transfer network.
Validation of the simulator results with the following studies:
"Using Canada's Abandoned Mines as a Source of Thermal Energy," dept. earth sciences, Carleton University, Ottawa;
Study of heat recovery systems on mine air exhausts combined with heat exchangers, University of Vancouver of Canada.

## Slide 20: 4. Simulation example Mining Infrastructure example - Éléonore Mine, Newmont
The Éléonore project is a large-scale mining site:
Team of around 800 employees
7000 t / day production target
Located in James Bay (Quebec)
Notes :
The energy consumption of the sources and loads in this example are estimated based on assumptions in order to simplify the analysis and to define approximate order of magnitude consumption values. These assumptions will have to be adequately confirmed prior to implementation of energy recovery techniques.
Reference: Éléonore 2018

## Slide 21: 4. Simulation example Site weather condition - Éléonore

## Slide 22: 4. Simulation example Systems available at the mine site
Plant Filtration System - (QS1_EP)
Filtration plant
Hot air exhaust - (QS2b)
Processing plant
Hot air exhaust - (QS2a)
Electric room
Local cooling - (QS3)
Surface garage
Heating of the building - (QC1)
Mine air inlet
Air heating - (QC2A)
Mine air inlet
Air heating - (QC2b)
Changing room
Water heating - (QC3)

## Slide 23: 4. Simulation example Energy available or consumed by the existing systems
Plant Filtration System - (QS1_EP)
40 650 MWh / year
Filtration plant
Hot air exhaust - (QS2b)
3 250 MWh / year
Processing plant
Hot air exhaust - (QS2a)
2 710 MWH / year
Electric room
Local cooling - (QS3)
5 820 MWH / year
Surface garage
Heating of the building - (QC1)
5 100 MWH / year
Mine air inlet
Air heating - (QC2A)
13 560 MWh / year
Mine air inlet
Air heating - (QC2b)
22 450 MWh / year
Changing room
Water heating - (QC3)
230 MWh / year

## Slide 24: 4. Simulation example Energy transfer between the QS1_EP and QC2B systems and the effect of the "NTU" of the exchangers
Number of heat exchanger transfer units | NTU = 1,25 | NTU = 0,5 | Difference
Energy transferred between systems(MWh / year) | 14 405 ( 64 % ) | 7 044 ( 31 % ) | 7 361
Fuel type | Propane |  | 
Fuel saved per year (L / year) | 1 945 000 | 951 500 | 993 500
GHG reduction (tonnes / year) | 3 000 | 1 470 | 1 530
Mandatory equipment
Mandatory equipment
Energy transferred between systems
Thermal loads (see loads tab)
Thermal sources (see sources tab)

## Slide 25: 4. Simulation example Performance of the heat transfer network and impact of the main pipe size
Heat transfer network information |  | 
Description | Variable | Value
Glycol type (Ethylene / propylene) | K | Ethylene
Safety factor for calculating pressure losses | F.S. | 25 %
Efficiency of the glycol network pump | Rpom | 75 %
Distance between thermal source and load [m] | DIS | 152
Minimum diameter of main pipe value calculated by the simulator (mm) | 150 mm |  | 
Selected line | 150 mm | 200 mm | Difference
Maximum pump power [kW] | 135 | 45 | 90
Annual energy consumed by the pump (MWh) | 385 | 135 | 250
Temperature (°C)

## Slide 26: 4. Simulation example Addition of the "load" system (QC3) and impact of the heat pump
Analysis of energy transfer to the QC3 "load" system |  |  | 
Equipment used to transfer energy | Heat pump (TP) | Exchanger NTU = 1 | Difference
Energy saved (MWh / year) | 181 ( 79 % ) | 45 ( 19 % ) | 136
Energy consumption (MWh / year) | 33 ( + 14 % ) | 0 | -33
Fuel type | Propane |  | 
Fuel saved (L / year) | 24 400 | 6 000 | 18 400
GHG reduction (tonnes / year) | 40 | 10 | 30
Mandatory equipment
Mandatory equipment
Optional equipment

## Slide 27: 4. Simulation example Systems available for associations
TFC : Hot network temperature (°C)
TFF : Cold network temperature (°C)
C : Flow capacity on the network side (kW / °C)
NTU : Number of transfer units for heat exchanger
"Loads" systems | Description |  | "Source" systems | Description
QC2b | Mine ventilation system service shaft |  | QS1_EP | Filtration system at the outlet of the treatment plant
QC3 | Changing room water heating system |  | QS2a | Treatment plant air exhaust system
QC2a | Mine ventilation system production shaft |  | QS2b | Filtration plant air exhaust system
QC1 | Garage ventilation system |  | QS3 | Electrical room powering the grinding mill systems

## Slide 28: 4. Simulation example Limitation of energy transfer during the year
Transfer limited by "load" systems

## Slide 29: 4. Simulation example Possible combinations for the energy recovery project
# | "Source" system |  |  |  | System "load" |  |  |  | Additional annual energy (MWh) |  | Savings | 
 | QS1_EP | QS2A | QS2B | QS3 | QC1 | QC2A | QC2B | QC3 | Heat transfer network | Heat pump | Energy (MWh) | GHG (tonnes)
1 | X NTU = 1,25 |  |  |  |  |  | X NTU = 1,25 Propane |  | 133 | 0 | 14 395 | 3 000
2 | X NTU = 1,25 |  |  |  |  |  | X NTU = 1,25 Propane | X TP Propane | 135 | 33 | 14 590 + 195 | 3 040 + 40
3 | X NTU = 1,25 |  |  | X NTU = 1,00 |  |  | X NTU = 1,25 Propane | X TP Propane | 166 | 39 | 15 266 + 675 | 3 180 + 140
4 | X NTU = 1,25 |  |  | X NTU = 1,00 |  | X NTU = 1,25 Propane | X NTU = 1,25 Propane | X TP Propane | 205 | 15 | 20 111 + 4 845 | 4 180 + 1 000
5 | X NTU = 1,25 |  | X NTU = 1,00 | X NTU = 1,00 |  | X NTU = 1,25 Propane | X NTU = 1,25 Propane | X TP Propane | 207 | 14 | 21 605 +1 494 | 4 490 + 310
6 | X NTU = 1,25 | X NTU = 1,00 | X NTU = 1,00 | X NTU = 1,00 |  | X NTU = 1,25 Propane | X NTU = 1,25 Propane | X TP Propane | 227 | 16 | 22 724 +1 119 | 4 730 + 240
7 | X NTU = 1,25 | X NTU = 1,00 | X NTU = 1,00 | X NTU = 1,00 | X TP Propane | X NTU = 1,25 Propane | X NTU = 1,25 Propane | X TP Propane | 258 | 240 | 24 785 + 2 061 | 5 160 +430

## Slide 30: 5. Simulation example Preliminary sizing of new equipment for the chosen combination
Coil (water / air)
UA = 181.5 kW / °C
Max flow network = 43.4 kg / s
System "load" = 195.1 kg / s
Heat pump (water / water)
Capacity: 25 kW
Max flow network = 1.4 kg / s
System "load" = 0.5 kg / s
Buffer tank:
Volume = 4.8 m³
Coil (water / air)
Exchange capacity (AU): 364.8 kW / °C Max flow network = 323 kg / s
System "load" = 364.8 kg / s
Coil (water / water)
UA = 444 kW / °C
Max flow network = 106.2 kg / s“
Source" system = 113.8 kg / s
Air conditioning system
included with coil (water / air)
Coil: UA = 54 kW / °C
Max flow network = 16.1 kg / s“
Source" system = 60.1 kg / s
Circulation pump
Max flow network = 0.5 kg / s

## Slide 31: 5. Simulation example Energy transferred between systems for the chosen combination
Energy transferred (MWh) | 20 111
Fuel type | Propane
Volume of fuel saved per year (L) | 2 690 000
GHG reduction (tonnes / year) | 4 180
Additional energy consumption (MWh) | 
Equipment | Consumption
Heat pump | 17 ( +0,1% )
Heat transfer network pump | 208 ( +1 % )
Energy transferred between systems

## Slide 32: 5. Next steps
Potential next steps in the development of the simulator:
Undertake a pilot project with the mining industry to verify the usability of the software.
Compare simulator results with actual consumption values at mining sites;
Improve the simulator based on stakeholder feedback;
Addition of an economic analysis to the program;
Addition of an optimization function to the program.

## Slide 33: Contact information
CanmetMINING :
  Yan Germain – yan.germain@canada.ca
  Enrique Acuña – enrique.acuna-duhart@canada.ca
CEMI:
  Charles Nyabeze – cnyabeze@cemi.ca